## Slide 1
AMD DEVELOPER HACKATHON · ACT II · UNICORN TRACK
qdot-live-twin
A live control console for a GPU-accelerated quantum-dot digital twin — with a triage agent that decides what's worth computing, and real bidirectional QCoDeS control.
COMPUTE AMD MI300X / ROCm
SIM BACKEND QArray (Rust)
FRAMEWORK QCoDeS-compatible
Built by K. Sarandega · github.com/k1151msarandega/SimQuantum-AMD-Developer-Hackathon

## Slide 2
RUBRIC COVERAGE
Where each judged criterion shows up, with evidence
Creativity & Originality
Bidirectional QCoDeS control — real settable Parameters, twin reacts live → Slide 7
Live-updating console, LabVIEW-style, not spinner-then-report → Slide 7
Triage agent visibly shedding load (SKIP) in real time → Slide 6
Product / Market Potential
QCoDeS-compatible today — any lab stack can subscribe or drive it, no rewrite → Slide 9
Honest status reporting: working vs. blocked, not oversold → Slide 9
Console shaped like something a lab would run next to real hardware → Slide 4, 9
Completeness
Full pipeline runs end-to-end: sim → estimator → triage → hardware adapter → console → Slide 4
All numbers measured on a real 2000-frame run, not projected → Slide 5
Known gap (LLM supervisor) disclosed with root cause, not hidden → Slide 6
Use of AMD Platforms
GPU-batched ensemble CNN inference runs on MI300X / ROCm → Slide 8
PyTorch batched inference is the mechanism behind the ~6x tail-latency win → Slide 5, 8
The pitch's central number traces directly back to this hardware, not around it → Slide 8
qdot-live-twin · AMD Developer Hackathon: Act II · Unicorn Track
2

## Slide 3
THE PROBLEM
Real quantum-dot labs generate data faster than models can honestly keep up
1
The fire hose
A stability-diagram stream that starts slow and accelerates — by design, so nothing downstream stays comfortable for long.
2
The naive fix breaks
Run full inference on everything, and backlog grows unboundedly the moment the stream outpaces compute — worst-case lag spikes with no ceiling.
3
The dishonest fix
Just make the model cheaper. That trades accuracy for speed everywhere, even when nothing is actually going wrong.
The real question isn't “how do we compute faster” — it's “what's actually worth computing, right now.”
qdot-live-twin · AMD Developer Hackathon: Act II · Unicorn Track
3

## Slide 4
HOW IT WORKS
COMPLETENESS
One real pipeline, five honest stages
01
QArray twin
Rust-backed DotArray sim emits ground-truth stability-diagram patches on a scripted (or live-overridden) gate trajectory.
→
02
Estimator
Serial CPU baseline vs. GPU-batched ensemble CNN on ROCm — same untrained weights, isolating compute cost from accuracy.
→
03
Triage agent
Rule-based FULL / CHEAP / SKIP decision from queue depth, staleness, and drift — tuned live by a background LLM supervisor.
→
04
QCoDeS twin
The same stream exposed as a real, settable QCoDeS Instrument — inject a voltage, the twin reacts on the next frame.
→
05
Control console
Streamlit UI that renders mid-run, not after — queue depth, tier routing, and supervisor reasoning, live.
Stage 04 is bidirectional, not a read-only pull — more on the next-but-one slide.
qdot-live-twin · AMD Developer Hackathon: Act II · Unicorn Track
4

## Slide 5
MEASURED, NOT CLAIMED
USE OF AMD PLATFORMS
COMPLETENESS
Every number below is from a real run against a real 2000-frame stream
Chart: Worst-case wall-clock lag, by mode (seconds)
| Serial (CPU) | GPU batched | + Triage | + Triage + LLM
Worst-case lag (s) | 0.117 | 0.02 | 0.021 | 0.021
~6x
tighter worst-case lag, GPU batched vs. serial CPU baseline (0.117s → 0.020s)
~4x
faster wall time end-to-end on the full 2000-frame run (30.8s → 8.1s)
~180x
faster single-diagram generation from QArray's Rust backend vs. JAX
Batching costs ~2ms of mean latency (a small, bounded wait to fill a batch) in exchange for a 6x tighter tail and 4x throughput — a deliberate, explainable trade, not a regression.
qdot-live-twin · AMD Developer Hackathon: Act II · Unicorn Track
5

## Slide 6
THE TRIAGE AGENT
COMPLETENESS
CREATIVITY & ORIGINALITY
The triage agent decides what's worth computing — and sheds load under backlog
Chart: Tier routing decisions per mode (micro-batches)
| + Triage | + Triage + LLM
FULL | 234 | 231
CHEAP | 13 | 18
SKIP | 47 | 43
Rule-based triage: fully working
Queue depth, time-since-full, and drift activity route each micro-batch to FULL / CHEAP / SKIP. SKIP genuinely drops frames — shown as distinct markers, not silently logged as completions.
LLM supervisor: designed, wired in, blocked
A background LLM reads backlog trends and re-tunes thresholds live. Fully implemented and integrated — currently blocked by a Fireworks account/deployment access issue on our end, not a design gap.
qdot-live-twin · AMD Developer Hackathon: Act II · Unicorn Track
6

## Slide 7
LIVE & BIDIRECTIONAL
CREATIVITY & ORIGINALITY
Not a read-only demo: turn a virtual knob, watch the twin react live
Live-updating console
LabVIEW-style: state renders as the run happens.
Chart and tier counts update every few micro-batches
No spinner-then-batch-report — the run is watchable
Supervisor reasoning streams in alongside the chart
Bidirectional QCoDeS control
vx_override / vy_override are real, settable QCoDeS Parameters.
Set an override — it writes into a shared, thread-safe voltage state
The very next pulled frame reflects the injected voltage
The drift detector flags anomalous frames live, in the same panel
This is the framework-compatibility pitch made real: a QCoDeS-based lab stack could drive this twin's gate voltages today, exactly as it would drive real hardware.
qdot-live-twin · AMD Developer Hackathon: Act II · Unicorn Track
7

## Slide 8
THE HARDWARE
USE OF AMD PLATFORMS
The MI300X isn't a checkbox — it's where the pitch's central number comes from
GPU-batched estimation
The ensemble CNN charge-state estimator runs as PyTorch/ROCm batched inference on the MI300X — the mechanism behind the ~6x tail-latency improvement over serial CPU.
Untrained weights, by design
The estimator's weights are intentionally untrained — this measures real compute cost and batching behavior under load, not model accuracy, which isn't the point of this demo.
Rust sim, GPU estimator
QArray's Rust backend generates ground-truth patches (~180x faster than JAX for single-frame gen); GPU work stays concentrated where batching actually pays off — the estimator.
COMPUTE AMD MI300X / ROCm STACK PyTorch batched inference SIM QArray (Rust)
qdot-live-twin · AMD Developer Hackathon: Act II · Unicorn Track
8

## Slide 9
WHERE THIS GOES
PRODUCT / MARKET POTENTIAL
This is the console shape a real lab would actually run next to a measurement
Working today
Serial + GPU-batched + rule-based triage, live-updating console, bidirectional QCoDeS control — all measured against a real 2000-frame stream, not mocked.
Honestly in progress
LLM-supervised threshold tuning is fully wired in and integration-tested; blocked on a Fireworks deployment/access issue, not a design gap.
Where this goes next
The QCoDeS adapter is the on-ramp: any QCoDeS-based lab stack can subscribe to this twin's stream or drive its gate voltages with no rewrite.
Thank you — github.com/k1151msarandega/SimQuantum-AMD-Developer-Hackathon
qdot-live-twin · AMD Developer Hackathon: Act II · Unicorn Track
9